## Slide 1
Lab Book 0.1. ModeSolver
Student:

## Slide 2: Instructions General
SCRIPTS
From GitHub 
  Fork the repo: https://github.com/cccanvas-upv/pic-upv-lab0.git
  Clone the repo using VSCode
Run the Jupyter Notebook:
  010_MODESOLVER_Student.ipynb
INSTRUCTIONS
We are going to work with different Cross-Sections. In general, we will need: Materials definitions and the Geometrical parameters of each Cross-section.
XY Cross-section
h
(height)
W (width)
Core
Cladding
W (width)
Core
Cladding
Slab
h_slab
h_core
shallow waveguide
deep waveguide

## Slide 3: Learning outcome #1 – Effective index of a waveguide
INSTRUCTOR:
Present Python and GDSFactory: materials, output, results.
Explain how to run a simulation for a particular cross-section.
Showcase how to change between shallow and deep waveguide.
Describe how to change the wavelength and width for the waveguide analysis.
Describe the outputs.
ALL EXAMPLE #1: waveguide width 1.2 µm, deep wvg, wavelength start and end same 1.55 µm  all ”Run”
ALL: Follow instructor, that will show how to 1) plot mode, 2) explore the results (neff …)
Document all your results (neff, plot fields of different modes, comparison between different polarizations…)

## Slide 4: Learning outcome #2 – Wavelength behavior Wavelength 1.5-1.6 µm (step 0.02 µm) – width 1.2 µm
Deep Waveguide.
En el que no tiene slab se propagan dos modos, ya que los que estén por debajo del índice de la cubierta.
El primer modo es TE y el segundo TM.
Si yo tuviera alguna forma de filtrar la polarización a la entrada del circuito entonces esa guía sería monomodo.
Es una guia monomodo. Podria ser monomodo TE o monomodo TM y propagaríamos el modo de orden 0 en ambas, TE0 o TM0.
El índice efectivo modela la propagación de la fase, como el índice efectivo váría, no es cte y tendremos dependencia de la longitude de onda. Operará de manera diferente.
El núcleo de nitruro de silicio, su índice es cercano a 2. Entonces vemos que no está muy confinado.
shallow waveguide
Paste plot here
slab = 150nm

## Slide 5: Thank you